## Slide 1
SoC Lab-FINAL Project
Arithmetic logic unit(ALU)
姓名:林宇廷
學號:C108110249
授課老師:謝瑞鴻教授

## Slide 2
大綱
介紹
TCL (Tool Command Language) File
製程比較
結論

## Slide 3
甚麼是ALU(Arithmetic logic unit)?
1.一種可對二進位整數執行算術運算或位元運算的組合邏輯數位電路
2. ALU 是許多類型的計算電路的基本部件，包括電腦的中央處理單元 （CPU）、浮點處理單元（FPU）和圖形處理單元（GPU) 。而單個CPU、FPU 或 GPU 可能包含多個 ALU。
介紹

## Slide 4
#======================================================
#
# Synopsys Synthesis Scripts (Design Vision dctcl mode)#
#======================================================
#======================================================
# Set Libraries
#======================================================
set search_path {/lib/SAED90_EDK/SAED_EDK90nm_ccs_models_hvt}
set synthetic_library dw_foundation.sldb
set link_library { saed90nm_typ_ht_hvt_ccs.db dw_foundation.sldb}
set target_library {saed90nm_typ_ht_hvt_ccs.db}
#======================================================
TCL File

## Slide 5
# Global Parameters
#======================================================
set DESIGN "alu“
set CLK_period 1
define_design_lib DESIGN_LIB -path ./LIB
#======================================================
# Read RTL Code
#======================================================
# ----- ALU -----
read_verilog -rtl /home/111-2/VLSI/C108110249/DESIGN/RTL/lab5/alu.v
current_design $DESIGN
#======================================================
# Global Setting
#======================================================
set_wire_load_mode enclosed

## Slide 6
#======================================================
# Set Design Constraints
#======================================================
create_clock -name "CLK" -period $CLK_period clk
set_input_delay [ expr $CLK_period*1 ] -clock CLK [all_inputs]
set_output_delay [ expr $CLK_period*1 ] -clock CLK [all_outputs]
set_load 0.03 [all_outputs]
#======================================================
# Optimization
#======================================================
Uniquify
set_fix_multiple_port_nets -all -buffer_constants
set_fix_hold [all_clocks]
compile_ultra
#======================================================

## Slide 7
#======================================================
# Output Reports
#======================================================
report_timing > Report/$DESIGN\.timing
report_area > Report/$DESIGN\.area
#======================================================
# Change Naming Rule
#======================================================
set bus_inference_style "%s\[%d\]“
set bus_naming_style "%s\[%d\]“
set hdlout_internal_busses true
change_names -hierarchy -rule Verilog
define_name_rules name_rule -allowed "a-z A-Z 0-9 _" -max_length 255 -type cell
define_name_rules name_rule -allowed "a-z A-Z 0-9 _[]" -max_length 255 -type net
define_name_rules name_rule -map {{"\\*cell\\*" "cell"}}
change_names -hierarchy -rules name_rule

## Slide 8
#======================================================
# Output Results
#======================================================
set verilogout_higher_designs_first true
write -format verilog -output Netlist/$DESIGN\_SYN.v –hierarchy
write_sdf -version 2.1 -context verilog -load_delay cell
Netlist/$DESIGN\_SYN.sdf
#======================================================
# Finish and Quit
#======================================================
check_design
exit

## Slide 9
Corner | Worst saed90nm_max_hvt_ccs | Typical saed90nm_typ_ht_hvt_ccs | Best saed90nm_min_lvt_ccs
Process(nm) | TSMC 90
Voltage(V) | 0.7 | 1.20 | 1.32
Temperature(°C) | 125 | 125 | -40
Clk | 2 | 2 | 2
Frequency(GHz) | 0.080 | 0.434 | 0.478
Area | 21178.9640 | 19348.1089 | 16330.7087
製程比較

## Slide 10
  使用Synopsys Design Compiler / Synthesis與Cell Library(TSMC90nm)模擬實驗結果。
  分析三種不同製程參數(Corner)的表現如下 :
    Slow Corner : 為了達到較低的電壓消耗，溫度則使用較高，但整體效能較差。
    Fast Corner : 以高效能為目標，消耗電壓較高，使用的溫度較低，但整體效能較好。
    Typical Corner : 以Slow和Fast電壓消耗與效能之間取得一個適當的平衡。
製程比較
硬體架構實驗 :

## Slide 11
THE END